## Slide 1: Mobile Unlock
Magnus Feuer
Jaguar Land Rover Open Software Technology Center

## Slide 2
Purpose
Use any smartphone
to unlock
any vehicle

## Slide 3
The user's story
An owner is travelling when a friend emails her to ask if he can borrow her car.
The owner brings up her guest driver app and sends a virtual car key, valid over the weekend, to her friend.
After the friend receives the key, he can walk up to the car to have his phone automatically unlock and start it.

## Slide 4
Overview – Demo system
Key mgmt
website
Android Unlock app
RasPi / RVI
Key management website [Cloud] Allow vehicle owners to provision and transmit keys to any android app
Android unlock app [Mobile Device] Runs a background service using keys to lock/unlock select vehicles
Unlock / Keyfob [Raspberry Pi] Receives, validates, and executes received lock/unlock command using a keyfob
Unlock
Keyfob

## Slide 5
Use Case
Vehicle owner sends access rights to a mobile device
Mobile device receives and stores key
Subscriber walks up to vehicle
Mobile device uses Bluetooth to unlock vehicle

## Slide 6
A guest driver is provisioned with vehicle id and target Android device
An RVI credential containing target service (jlr.com/[VIN]/unlock) is created and signed by the root certificate
RVI credential is transmitted from website to target Android device using RVI
Unlock app on Android device receives credential and stores it as an RVI certificate
Key provisioning
Android
Website
Key Provisioning
RVI
RVI SDK
Unlock App

## Slide 7
GPIO
RVI
Unlock service detects vehicle presence
Unlock service sends unlock command to Android RVI
RVI forwards command, with provisioned credentials, to Raspberry RVI using Bluetooth
Raspberry RVI validates command and forwards it to Unlock app
Unlock app manipulates GPIO pins to press the unlock button on key fob
Vehicle
Android
Unlock App
RVI
Key fob
Unlock Service
Raspberry Pi
iBeacon RVI / IPv6

## Slide 8: Thank You
Magnus Feuer System Architect – Open Software Initiative
mfeuer@jaguarlandrover.com
+1-949-294 7871